FLASHDOC.TXT UPDATE 2/9/93:

FILE MANAGER works with FMAP1 and 
recognizes the extra (D:) drive 
automatically.  Just load FM.COM from 
the file manager card into D: of FMAP1 
and anytime you want to use it type FM 
<enter> from the D: drive.

HARD DISK
The FMAP1 driver (FLASHDRV.SYS) 
unfortunately has the same DOS name as 
the driver used by the hard disk drive 
for the Port.  If you want to use both 
the FMAP1 and a hard drive you'll have 
to change the name of one of the 
drivers.

RAM CARDS
RAM cards which are not write protected 
should not be used when FLASHDRV.SYS 
for the FMAP1 is active in C: or hidden 
in the system RAM.  The FMAP1 driver 
writes to the card to set control logic 
latches in the on-card state machine 
before data can be read from it.  For 
this reason if you plug in a standard 
RAM card with FLASHDRV.SYS active, you 
will write to the RAM card even when 
you think you are only reading.  To 
avoid losing RAM card files you should 
either turn the card write protect ON 
or delete *.SYS from C: and reboot to 
also eliminate it from system RAM.  You 
can test for its presense in system RAM 
by typing D: <enter>.  If the cursor 
switches to D the driver still lives in 
system RAM;  if the message "Invalid 
drive" appears the driver is gone.  A 
convenient way to get rid if the driver 
when changing from FMAP1 to an 
unprotected RAM card is to put an 
AUTOEXEC.BAT file on the RAM card with 
the statement DEL C:*.SYS in it.  Then 
simply reboot twice every time you 
switch from FMAP1 to a RAM card with 
write protect OFF.  The first reboot 
removes the driver from C: and the 
second removes it from system RAM.

NO CARD
If you want to use the Port without any 
memory card after using the FMAP1 you 
should do DEL C:*.SYS to remove the 
driver from C:.  Otherwise if you 
reboot the driver will look for some 
memory card, find none, and lockup 
until some card is inserted.

DIR
DIR D: is still valuable for listing 
active files and directories but the 
free space number reported will be too 
high because DOS cannot distinguish 
between used and clean sectors.

MEMORY FULL
This error statement will occur when 
attempting to clean if the C: drive is 
over 32K leaving insufficient system 
RAM to retain card block data while a 
block is flash erased.  To fix a MEMORY 
FULL error, backup files on C: and do 
FDISK 32 or less;  then CLEAN.

FORMAT
This DOS command has no effect on FMAP1 
cards and is not needed.  The cards are 
shipped pre-formatted and ready to use.  
If there is ever a need to reformat the